## Slide 1: Unit I Computer Evolution and Arithmetic

## Slide 2: Ancient era
Abacus
Napiers bones
What was before this ?

## Slide 3: Zero Generation : Mechanical Era (1600-1940)
  Wilhelm Schickhard and Blaise Pascal (1623-1642)
: built a mechanical counter with carry

## Slide 4
Charles Babbage
originated the concept of a programmable computer.
Considered the "father of the computer",
he conceptualized and invented the first mechanical computer in 1833
he realized that a much more general design, an Analytical Engine, was possible. The input of programs and data was to be provided to the machine via punched cards, a method being used at the time in mechanical looms such as the Jacquard loom.

## Slide 5
Babbage’s Differential Engine
This machine used the decimal number system and was powered by cranking a handle. To approximate logarithmic and trigonometric functions, by polynomials

## Slide 6
  George Boole (1847)
Boolean algebra is the subarea of algebra in which the values of the variables are the truth values true and false, usually denoted 1 and 0 respectively.
elementary algebra uses values of the variables are numbers & operations are addition and multiplication,
Boolean algebra operations are the conjunction and(∧), the disjunction or ( ∨), and the negation not (¬).

## Slide 7
  Herman Hollerith (1880) – Punched Cards

## Slide 8
  Konrad Zuse (1938):Automatic Calculating Machine based on Electromagnetic mechanism

## Slide 9: First Generation (1946-1957): Vacuum Tubes
Late 1940s and 1950s
Stored-program computers
Programmed in assembly language
Used magnetic devices and earlier forms of memories
Examples: IAS, ENIAC, EDVAC, UNIVAC, Mark I, IBM 701

## Slide 10
1943-44: John Mauchly (professor) and J. Presper Eckert (graduate student) built ENIAC (Electronic Numerical Integrator and Computer) at U. Penn.
1944: Howard Aiken used “separate data and program memories” in MARK I computer – Harvard Architecture.
1945-52: John von Neumann proposed a “stored program computer” EDVAC (Electronic Discrete Variable Computer) – Von Neumann Architecture – use the same memory for program and data.

## Slide 11: ENIAC – background
Electronic Numerical Integrator And Computer
Eckert and Mauchly
University of Pennsylvania
Trajectory tables for weapons
Started 1943
Finished 1946
  Too late for war effort
Used until 1955

## Slide 12: ENIAC - details
Decimal number system used (not binary)
20 accumulators of 10 digits
Programmed manually by switches : programming by Plugging and Unplugging of switches ,Results were punched on cards or printed on type writer
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second

## Slide 14
IAS
von Neumann and his colleagues , designed in 1952

## Slide 15: Commercial Computers
1947 - Eckert-Mauchly Computer Corporation
UNIVAC I (Universal Automatic Computer)
US Bureau of Census 1950 calculations
Became part of Sperry-Rand Corporation
Birth of IBM and Sperry in 1950s.
  1953-IBM 701 for scientific calculations
  1955-IBM 702 for Business Application

## Slide 16: Second Generation (1955-1965) :Transistors
Replaced vacuum tubes
Smaller, Cheaper
Less heat dissipation
Solid State device
Made from Silicon (Sand)
Invented 1947 at Bell Labs
  Multiplexer, Data Channel
  Concept of System Software

## Slide 17
Magnetic core memories
Floating-point arithmetic
High-level languages used: ALGOL, COBOL and FORTRAN
System software: compilers, subroutine libraries, batch processing
Examples:
IBM 7000, IBM 7094, DEC – 1957, PDP-1

## Slide 19: Third Generation (1965-1971) : Integrated Circuit
Literally - “small electronics”
A computer is made up of gates, memory cells and interconnections
Integrated circuit (IC) technology
Semiconductor memories
Memory hierarchy, virtual memories and caches
Time-sharing OS
Parallel processing and pipelining
Microprogramming
Examples:
IBM 360 & 370, ILLIAC IV, DEC PDP8 and VAX, Amdahl 470

## Slide 20: All Generations of Computer
Vacuum tube - 1946-1957
Transistor - 1958-1964
Small scale integration - 1965 on
  Up to 100 devices on a chip
Medium scale integration - to 1971
  100-3,000 devices on a chip
Large scale integration - 1971-1977
  3,000 - 100,000 devices on a chip
Very large scale integration - 1978 to date
  100,000 - 100,000,000 devices on a chip
Ultra large scale integration
  Over 100,000,000 devices on a chip

## Slide 21
Intel
1971 - 4004
  First microprocessor
  All CPU components on a single chip
  4 bit
Followed in 1972 by 8008
  8 bit
  Both designed for specific applications
1974 - 8080
  Intel’s first general purpose microprocessor

## Slide 23: 5th generation

## Slide 24
Intel
1971 - 4004
  First microprocessor
  All CPU components on a single chip
  4 bit
Followed in 1972 by 8008
  8 bit
  Both designed for specific applications
1974 - 8080
  Intel’s first general purpose microprocessor

## Slide 25: Pentium Evolution (1)
8080
  first general purpose microprocessor
  8 bit data path
  Used in first personal computer – Altair
8086
  much more powerful
  16 bit
  instruction cache, prefetch few instructions
  8088 (8 bit external bus) used in first IBM PC
80286
  16 Mbyte memory addressable
  up from 1Mb

## Slide 26: Pentium Evolution (2)
80386
  32 bit
  Support for multitasking
80486
  sophisticated powerful cache and instruction pipelining
  built in maths co-processor
Pentium
  Superscalar
  Multiple instructions executed in parallel

## Slide 27: Pentium Evolution (3)
Pentium Pro
  Increased superscalar organization
  Aggressive register renaming
  branch prediction
  data flow analysis
  speculative execution

## Slide 28
32-bit processors: P5 microarchitecture , Pentium with MMX Technology
32-bit processors: P6/Pentium M microarchitecture
  Pentium Pro ,II, Celeron,III,M, Intel Core, Dual-Core Xeon LV
32-bit processors: NetBurst microarchitecture
  Pentium 4, Xeon, 4F
64-bit processors: IA-64
  Itanium 1,2
64-bit processors: Intel 64 – NetBurst microarchitecture
  Pentium 4F,D, Xeon
64-bit processors: Intel 64 – Core microarchitecture
  Xeon , Intel Core 2 , Dual-Core
64-bit processors: Intel 64 – Nehalem microarchitecture
  Intel Pentium ,i3,i5,i7, Xeon
64-bit processors: Intel 64 – Sandy Bridge / Ivy Bridge microarchitecture
  Celeron , Pentium , Core i3 ,i5, i7(3.50 GHz price Rs 23K,)
64-bit processors: Intel 64 – Haswell microarchitecture

## Slide 29: Microprocessor manufacturers
AMD
ARM Holdings
Cyrix
Freescale
Intel
IBM
Marvell
NexGen
Nvidia Tegra
Oracle (previously Sun)
OWC
Qualcomm
Rise Technology
Samsung
SigmaTel
Sonnet
Texas Instruments
Transmeta
tilera
Via (Centaur Technology division)
winchip

## Slide 30: Generations of Computer
Generation | Era | Basic element used | Examples
0 | Till 1946 | Mechanical counter | Mechanical counter with carry
1 | 1946-57 | Vacuum Tubes | ENIAC, EDVAC, UNIVAC
2 | 1958-64 | Transistor | IBM 7000, IBM 7094, DEC- 1957, PDP-1
3 | 1965-71 | Integrated Circuit (SSI,MSI) | IBM 360 and 370, DEC PDP8
4 | 1972-77 | Microprocessors (LSI) | 4004,8085,8086
5 | 1978-91 | Microprocessors (VLSI,ULSI) | Pentium,…. i7

## Slide 31
Ref: Stallings