## Slide 1: top level view of computer
Block diagram of computer

## Slide 2: Computer Components: Top-Level View

## Slide 3: CPU
Block diagram

## Slide 4
Main components in CPU
ALU
Registers
Control unit
Function of CPU
  Fetch instructions
  Interpret/decode instructions
  Fetch data /operand
  Process data
  Write Processed data

## Slide 5: ALU
An arithmetic logic unit (ALU) is a combinational digital electronic circuit that performs arithmetic and bitwise logical operations on integer binary numbers.
Other types floating-point unit (FPU), which operates on floating point numbers and graphics processing units(GPUs).
A single CPU, FPU or GPU may contain multiple ALUs.

## Slide 6
Registers
-Small set of high speed storage( memory) locations inside the CPU
  Used for Temporary storage for data and control information ( Analogy : grocery in house & grocery shop)
Two types of registers
  User-visible
    These Can be used in assembly-level instructions and are thus “visible” to the user
– Control and status registers
    Used to control the operation of the CPU
    Most are not visible to the user

## Slide 7
User Visible Registers
  General purpose
    Can be assigned a variety of functions
    Ideally, they are for the operations within the instructions
  Data
    These registers only hold data
  Address
    These registers only hold address information
    Examples: address registers, segment registers, stack pointers, index registers
  Condition codes ( flag register, Status register)
    Visible to the user but values set by the CPU as the result of performing operations
    Example code bits: zero, positive, overflow
    Bit values are used as the basis for conditional jump instructions

## Slide 8
Simplified CPU operation

## Slide 9
Animation of how processor executes instructions
When CPU is turned ON , it starts fetching instruction from address 0000 ,
So it loads PC with 0000

## Slide 10
Contents of PC Is transferred to MAR

## Slide 11
Contents of MAR are sent on address bus

## Slide 12
CU then sends read ( RD) signal on control bus

## Slide 13
Memory sends contents of address 0000 on data bus which is laded in MBR

## Slide 14
CU transfers MBR contents to instruction register IR , since it is an instruction

## Slide 15
CU decodes instruction , it finds that R1 is to be added in R0 and
result to be stored in R0

## Slide 16
CU gives R0 and R1 contents to ALU and gives add signal to ALU

## Slide 17
The result of addition is transferred by CU in R0

## Slide 18
CU then increments PC by 1 to fetch next instruction from 0001

## Slide 19
Instruction cycle detailed

## Slide 20
Instruction cycle with interrupt handling
all computers provide a mechanism by which other modules (I/O, memory) may interrupt the normal processing of instructions by the processor.
To take care of some other functions ( such as key pressed on keyboard , some error occurred etc)
Interrupt is checked after each instruction is executed.

## Slide 21
INTERCONNECTION STRUCTURES
A computer consists of a set of components or modules of three basic types (processor, memory, I/O) that communicate with each other.
So, a computer is a network of basic modules. Thus, there must be paths for connecting the modules. The collection of paths connecting the various modules is called the interconnection structure.

## Slide 22
BUS INTERCONNECTION A bus is a communication pathway connecting two or more devices.
it is a shared transmission medium. Multiple devices connect to the bus, and a signal transmitted by any one device is available for reception by all other devices attached to the bus.
If two devices transmit during the same time period, their signals will overlap and become garbled. Thus, only one device at a time can successfully transmit.
Typically, a bus consists of multiple communication pathways, or lines. Each line is capable of transmitting signals representing binary 1 and binary 0.. Taken together, several lines of a bus can be used to transmit binary digits simultaneously (in parallel). For example, an 8-bit unit of data can be transmitted over eight bus lines

## Slide 23
Address lines:
Only CPU sends address of memory location or I/O device from where it wants to read or to write data.
Control lines :
signals sent by CPU or I/O devices to inform what operation is being carried out

## Slide 24
Single bus structure
Simple but slow

## Slide 25
Multiple-Bus Hierarchies If a great number of devices are connected to the bus, performance will suffer.There are two main causes: 1. In general, the more devices attached to the bus, the greater the bus length and hence the greater the propagation delay. 2. The bus may become a bottleneck as the aggregate data transfer demand approaches the capacity of the bus.
Solution : most computer systems use multiple buses, generally laid out in a hierarchy.

## Slide 26
Traditional bus architecture
This architecture is efficient but begins to break down as higher and higher performance I/O devices are connected . eg graphics card

## Slide 27
Solution:
a high speed bus is added in the system, requiring only a bridge between the processor’s bus and the high-speed bus.
The cache controller is integrated into a bridge, or buffering device, that connects to the high-speed bus

## Slide 28
advantage of this arrangement is
the high-speed bus brings high demand devices into closely interacting with the processor and at the same time is independent of the processor. Thus, differences in processor and high-speed bus speeds and other signals are tolerated.
Changes in processor architecture do not affect the high-speed bus, and vice versa.

## Slide 30
Elements of Bus Design

## Slide 31
Bus type:
Dedicated and multiplexed.
A dedicated bus line is permanently assigned either to one function.
Multiplexed bus can do different function at different times
8086 uses multiplexed address & data bus

## Slide 32
Synchronized
All devices are Synchronized With each other using clock signal
Synchronous timing is simpler to implement and test . So used in almost all computers
Eg memory read operation by CPU

## Slide 33
Address bus size
determines number of memory locations that can be accessed i.e. amount of memory that can be connected to CPU
N address lines can access memory up to 2 N
16 bit address bus can access 2 16 = 65535 = 64k memory
Data bus size
Determines the size of data that can be transferred at a time
8 bit data bus can transfer 8 bits at a time